Recycling

By Roy A. Hartman, BS, MBA, PhD

I  INTRODUCTION

Recycling, collection, processing, and reuse of materials that would otherwise be thrown away. Materials ranging from precious metals to broken glass, from old newspapers to plastic spoons, can be recycled. The recycling process reclaims the original material and uses it in new products.

In general, using recycled materials to make new products costs less and requires less energy than using new materials. Recycling can also reduce pollution, either by reducing the demand for high-pollution alternatives or by minimizing the amount of pollution produced during the manufacturing process. Recycling decreases the amount of land needed for trash dumps by reducing the volume of discarded waste.

Recycling can be done internally (within a company) or externally (after a product is sold and used). In the paper industry, for example, internal recycling occurs when leftover stock and trimmings are salvaged to help make more new product. Since the recovered material never left the manufacturing plant, the final product is said to contain preconsumer waste. External recycling occurs when materials used by the customer are returned for processing into new products. Materials ready to be recycled in this manner, such as empty beverage containers, are called postconsumer waste.

II  TYPES OF MATERIALS RECYCLED

Just about any material can be recycled. On an industrial scale, the most commonly recycled materials are those that are used in large quantities—metals such as steel and aluminum, plastics, paper, glass, and certain chemicals.

A  Steel

Approximately 64 percent of all steel is recycled, making it one of the world’s most recycled materials. In 2000 31 billion steel cans, weighing 2.4 million metric tons (2.6 million U.S. tons), were used in the United States, of which 58.4 percent were recycled. In 2000 more than 60 million metric tons (70 million U.S. tons) of scrap steel were recycled in the United States.

B  Aluminum

The U.S. aluminum industry has recognized the advantage of a domestic aluminum supply and has established systems for collection, transportation, and processing. For this reason, aluminum cans almost always produce a profit in community recycling programs. A number of states require deposits for beverage containers and have established redemption centers at supermarkets. The overall recycling rate of all forms of aluminum is about 35 percent.

Cans brought to collection centers are crushed, baled, and shipped to regional mills or reclamation plants. The cans are then shredded to reduce volume and heated to remove coatings and moisture. Next, they are put into a furnace, melted, and formed into ingots, or bars, weighing 10,000 kg (30,000 lb) or more. The ingots go to another mill to be rolled into sheets. The sheets are sent to a container plant and cut into disks from which new cans are formed. The cans are printed with the beverage makers’ logos and are shipped (with tops separate) to the filling plant.

C  Plastics

The recycling process for plastic normally involves cleaning it, shredding it into flakes, then melting the flakes into pellets. The pellets are melted into a final product. Some products work best with only a small percentage of recycled content. Other products, such as HDPE plastic milk cases, can be made successfully with 100 percent recycled content. The plastic container industry has concentrated on weight reduction and source reduction. For example, the one-gallon HDPE milk container that weighed about 120 gm (about 4.2 oz) in the 1960s weighed just 65 gm (about 2.3 oz) in 1996.

D  Paper and Paper Products

Paper products that can be recycled include cardboard containers, wrapping paper, and office paper. The most commonly recycled paper product is newsprint.

In newspaper recycling, old newspapers are collected and searched for contaminants such as plastic bags and aluminum foil. The paper goes to a processing plant where it is mixed with hot water and turned into pulp in a machine that works much like a big kitchen blender. The pulp is screened and filtered to remove smaller contaminants. The pulp then goes to a large vat where the ink separates from the paper fibers and floats to the surface. The ink is skimmed off, dried and reused as ink or burned as boiler fuel. The cleaned pulp is mixed with new wood fibers to be made into paper again.

E  Glass

Scrap glass taken from the glass manufacturing process, called cullet, has been internally recycled for years. The scrap glass is economical to use as a raw material because it melts at lower temperatures than other raw materials, thus saving fuel and operating costs.

Glass that is to be recycled must be relatively free from impurities and sorted by color. Glass containers are the most commonly recycled form of glass, and their colors are flint (clear), amber (brown), and green. Other glass, such as window glass, pottery, and cooking utensils, are considered contaminants because they have different compositions than glass used in containers. The recycled glass is melted in a furnace and formed into new products.

F  Chemicals and Hazardous Waste

Household hazardous wastes include drain cleaners, oven cleaners, window cleaners, disinfectants, motor oil, paints, paint thinners, and pesticides. Most municipalities ban hazardous waste from the regular trash. Periodically, citizens are alerted that they can take their hazardous waste to a collection point where trained workers sort it, recycle what they can, and package the remainder in special leak-proof containers called lab packs, for safe disposal. Typical materials recycled from the collection drives are motor oil, paint, antifreeze, and tires.

G  Nuclear Waste

Certain types of nuclear waste can be recycled, while other types are considered too dangerous to recycle. Low-level wastes include radioactive material from research activities, medical wastes, and contaminated machinery from nuclear reactors. Nickel is the major metal of construction in the nuclear power field and much of it is recycled after surface contamination has been removed.

High-level wastes come from the reprocessing of spent fuel (partially depleted reactor fuel) and from the processing of nuclear weapons. These wastes emit gamma radiation, which can cause birth defects, disease, and death. High-level nuclear waste is so toxic it is not normally recycled. Instead, it is fused into inert glass tubes encased in stainless steel cylinders, which are then stored underground.

III  REASONS FOR RECYCLING

Rare materials, such as gold and silver, are recycled because acquiring new supplies is expensive. Other materials may not be as expensive to replace, but they are recycled to conserve energy, reduce pollution, conserve land, and to save money.

A  Resource Conservation

Recycling conserves natural resources by reducing the need for new material. Some natural resources are renewable, meaning they can be replaced, and some are not. Paper, corrugated board, and other paper products come from renewable timber sources. Trees harvested to make those products can be replaced by growing more trees. Iron and aluminum come from nonrenewable ore deposits. Once a deposit is mined, it cannot be replaced.

B  Energy Conservation

Recycling saves energy by reducing the need to process new material, which usually requires more energy than the recycling process. To make an aluminum can from recycled metal takes only 5 percent of the total energy needed to produce the same aluminum can from unrecycled materials, a 95 percent energy savings. Recycled paper and paperboard require 75 percent less energy to produce than new products. Significant energy savings result in the recycling of steel and glass, as well.

C  Pollution Reduction

Recycling reduces pollution because recycling a product creates less pollution than producing a new one. For every ton of newspaper recycled, 7 fewer kg (16 lb) of air pollutants are pumped into the atmosphere. Recycling can also reduce pollution by recycling safer products to replace those that pollute. Some countries still use chlorofluorocarbons (CFCs) to manufacture foam products such as cups and plates. Many scientists suspect that CFCs harm the atmosphere’s protective layer of ozone. Using recycled plastic instead for those products eliminates the creation of harmful CFCs.

D  Land Conservation

Recycling saves valuable landfill space, land that must be set aside for dumping trash, construction debris, and yard waste (see Solid Waste Disposal: Landfill). In the United States, each person on average discards almost a ton of municipal solid waste (MSW) per year. MSW is raw, untreated garbage of the kind discarded by homes and small businesses. Waste from industry and agriculture normally is not part of MSW, but construction and demolition wastes are. The United States has the highest MSW discard level of any country in the world.

Solid waste can also be burned instead of buried in the ground. Typically, waste-to-energy (WTE) facilities burn trash to heat water for steam-turbine electrical generators. This WTE recycling keeps another 14.5 percent of municipal solid waste out of the landfills.

E  Economic Savings

Recycling in the short term is not always economically profitable or a break-even financial operation. Most experts contend, however, that the economic consequences of recycling are positive in the long term. Recycling will save money if potential landfill sites are used for more productive purposes and by reducing the number of pollution-related illnesses.

© 1993-2003 Microsoft Corporation. All rights reserved.